## Slide 1: PID Tuning for a UAV using Reinforcement Learning
Grande Alessandro Francesco
Truppi Federico
Notes: Our project is about PID tuning for a UAV using Reinforcement Learning. (Il nostro progetto parla del PID tuning for a UAV usining Reinforcement Learning).

## Slide 2: Introduction
Goals;
Mathematical model;
UAV Control;
Reinforcement Learning;
Simulink;
Results.
Notes: We will see our goals, the mathematical model choosen for the uav, the loop control of the uav, general informations about reinforcement learning and the methods used, the simulink block diagram and finally our results

## Slide 3: Goals
Optimizing Control gains
Applying reinforcement learning for adaptive tuning
Improving UAV stability and tracking
Notes: One of the challenges in implementing a PID-based control is not so much the code itself, but the tuning of the gains. (Uno dei problemi nel implementare un controllo basato sul PID non è tanto il codice ma il tuning dei parametri). For this reason, RL was used to find the gains in adptive way, in order to improve stability and tracking. (Per questa ragione è stato utilizzato il RL per trovare in modo adattativo i guadagni. in moda di migliorare la stabilità e il tracking).

## Slide 4: Mathematical Model
x, y, z: coordinates of the drone position in the inertial reference system;
x’, y’, z’: linear velocities along the axes x, y, z;
ϕ: Roll angle (rotation about the x axis of the body);
θ: Pitch angle (rotation about the y axis of the body);
ψ: Yaw angle (rotation about the z axis of the body);
p, q, r: angular velocities around the x, y, z axes of the body;• m: drone mass;
Ixx, Iyy, Izz : moments of inertia with respect to the x, y, z axes;
Ax, Ay, Az : coefficients of friction (linear) in the respective axes;
U1: total thrust force generated by the propellers;
U2: torque around the x axis (roll);
U3: torque around the y axis (pitching);
U4: torque around the z axis (yaw).
Notes: The first step is to obtain the mathematical model of the UAV, derived by considering two reference frames: one fixed to the ground and one attached to the drone. The first three equations describe the translational dynamics, while the last three describe the rotational dynamics of the UAV. The inputs of the drone are the thrust generated along the z-axis and the three torques around the x, y, and z axes. (Il primo step è trovato il modello matematico del UAV, ottenuto considerando 2 sistemi di riferimento, uno terna base e uno terna solidale al drone. Le prime tre equazioni descrivono la dinamica traslazionale, mentre le ultime tre la dinamica rotazionale dell'uav. )
The first step to reach the mathematical model is to consider the quadcopter as a rigid body moving in the space. We must set up some different reference systems. The first one is the Earth-fixed (IF) reference system, that is, a non-rotating inertial system with Z-axis pointing towards the south pole. The second one is the Body fixed (BF) reference system, that is, a reference system translating with the body itself and centered on the center of mass of the quadcopter. Thanks to them, it is possible to trace the translational coordinates and to know the dynamics of the attitude, respectively. As we can see in the final model the first three equations describe the translational dynamics, while the last three the rotational dynamics of the uav.

## Slide 5: UAV Control
Cascade control:
Inner loop → attitude control;
Outer loop → position control;
Notes: The proposed control is a cascaded control with two control loops: an inner loop and an outer loop. This separation is possible since, by assumption, the attitude dynamics are faster than the position dynamics. Il controllo proposto è un controllo in cascata con due loop di controllo, il loop interno e loop esterno. Questa separazione è possibile dato che per ipotesi la dinamica dell'orientamento è piu' veloce della dinamica della posizione.

## Slide 6: UAV Control: Outer Loop
PD Controller:
Input
Output
Notes: The PD controller of the outer loop receives the position and velocity errors and generates an acceleration reference. Il PD del loop esterno riceve l'errore di posizione e di velocità è produce un riferimento di accelerazione.

## Slide 7: UAV Control: Desired Angles
To obtain the desired angles:
For simplicity, the desired yaw angle is assumed to be zero.
Notes: After obtaining the acceleration references, the desired angles are calculated using these two equations, while, for simplicity, the yaw reference angle is set to zero. (Un volta trovati i referimenti di accelerazione, tramite queste due equazioni sono stati ottenuti gli angoli desiderati e per semplificare l'angolo di riferimento yaw è assunto uguale a zero)
To obtain the desired horizontal accelerations ades,x and ades,y, the drone must tilt appropriately. Under the assumption of small angles and almost-steady-state dynamics, the roll (ϕdes) and pitch (θdes) references are obtained through kinematic inversion:

## Slide 8: UAV Control: Inner loop
PD Controller:
Input
Output
Notes: The inner loop takes the angular error and angular velocity error to generate the torques. (Il loop interno prende l'errore angolare e l'errore di velocità angolare per generate le coppie.)
The inner loop (attitude control) takes the desired angles and current orientation as input and generates control moments for roll, pitch, and yaw.

## Slide 9: Reinforcement Learning
Agent: the entity that learns and takes actions within the environment;
Environment: the context in which the agent operates, providing feedback based on the agent’s actions;
Policy: the strategy or the mapping that dictates how an agent should act in a given state;
Action: a decision made by the agent within the environment;
Goal: the objective of the agent, typically to maximize the cumulative reward overtime.
Reward: feedback provided by the environment indicating the quality of the agent’s action;
Action
Reward
Environment
Notes: Reinforcement Learning is a branch of Machine Learning that focuses on how an intelligent agent should take actions in an environment to maximize a reward signal. The agent develops a set of rules or policies that help it decide which action to take next in order to achieve the optimal cumulative reward. (IL Reinforcement learning è un regione del machine learning che si occupa di come un agente intelligente debba compiere delle azione sull'ambiente per massimizzare un segnale di ricompensa. L’agente crea un insieme di regole o poliche che lo aiutano a decidere quale azione intraprendere successivamente per ottenere la ricompensa cumulativa ottimale.)
Reinforcement learning (RL) is an interdisciplinary area of machine learning and optimal control that is concerned with how an intelligent agent should take actions in a dynamic environment to maximize a reward signal through trial and error. The agent creates a set of if-then rules or policies which help it to decide which action to take next to achieve the optimal cumulative reward. The agent must also choose between further exploring the environment to learn new state-action rewards or selecting known high-reward actions from a given state, the so-called exploration-exploitation trade-off. In the slide we can see the main elements of reinforcement learning.

## Slide 10: Deep Deterministic Policy Gradient (DDPG)
Off-policy
Actor-critic
Continuous action-space
Deterministic
Notes: The first one is DDPG. This is an actor-critic method, as it involves two agents: the actor, which is the network that decides which action to take, and the critic, the network that informs the actor about the quality of the action and how it should be adjusted. It is deterministic because the actor is a policy network that takes the state as input and produces the exact action. Another important feature is that DDPG is an off-policy method, meaning that it allows an agent to learn a policy (the target policy) that is different from the policy used to generate the data (the behavior policy). (Il primo è il DDPG. Questo è un metodo actor-critic, perché prevede due agenti: l’actor, la rete che decide quale azione intraprendere, e il critic, la rete che informa l’actor su quanto sia stata buona l’azione e come dovrebbe aggiustarla. È deterministico perché l’actor è una rete di policy che prende lo stato come input e produce l’azione esatta. Un’altra caratteristica importante è che il DDPG è un metodo off-policy, ossia un metodo che permette a un agente di apprendere una policy (policy target) diversa dalla policy usata per generare i dati (behavior policy).)
In our work we used three RL methods. The first one is the ddpg. This is an actor-critic method because we have two agents: the actor, the network that decides which action should be taken, and the critic, the network that informs the actor how good was the action and how it should be adjusted, using a Q-function.
It’s deterministic because the actor is a policy network that takes the state as input and outputs the exact action, instead of a probability distribution over actions.
Another important feature is that ddpg is an off-policy method: a method that allows an agent to learn a policy (target policy) that is different from the policy used to generate the data (behavior policy). While the behavior policy generates control actions for observed environment states, the target policy is trained iteratively using the subsequent outcome of the action.
In other words, off-policy RL decouples the data collection process from policy training.

## Slide 11: Twin Delayed Deep Deterministic Policy Gradient (TD3)
Off-policy
Actor-critic
Continuous action-space
Deterministic
Twin Critics
Delayed Policy Updates
Clipped noise
Notes: TD3 uses two separate Q-networks (critics) instead of one. The actor (policy network) is updated less frequently than the critics, preventing the policy from chasing overly noisy value estimates. The clipped noise allows TD3 to be more stable than DDPG. (TD3 utilizza due reti Q separate (critic) invece di una sola. L’actor (rete di policy) viene aggiornato meno frequentemente rispetto al critic, evitando che la policy “insegua” stime di valore troppo rumorose. Il clipped noise permette a TD3 di essere più stabile rispetto al DDPG.
Twin Q networks (Twin Critics): TD3 uses two separate Q-networks (critics) instead of one, the minimum of the two Q-values is used for the target. This reduces the overestimation bias found in DDPG. The actor (policy network) is updated less frequently than the critic, this prevents the policy from chasing noisy value estimates.
The clipped noise allows TD3 to be more stable than DDPG.

## Slide 12: Soft Actor Critic (SAC)
Off-policy
Actor-critic
Continuous action-space
Stochastic (Policy Entropy)
Twin critic
Notes: The SAC agent, unlike standard reinforcement learning, will not try to maximize just the expected reward, but also a policy entropy. This lets the actor output a probability distribution (usually a Gaussian distribution) over actions, and makes the agent prefer exploratory actions instead of deterministic ones.
(l’agente SAC non cercherà di massimizzare solo la ricompensa attesa, ma anche l’entropia della policy. Questo permette all’actor di produrre una distribuzione di probabilità (di solito una distribuzione gaussiana) sulle azioni e fa sì che l’agente preferisca azioni esplorative anziché azioni deterministiche e greedy.)

## Slide 13: Methods Confrontation Table
Notes: This is just a brief summary of the three algorithms.

## Slide 14: Simulink
Notes: This is the block scheme of the system. It includes the drone, the two control loops, and the inputs. ( Questo è lo schema a blocchi del sistema. Abbiamo il drone, i due loop di controllo e gli ingressi.)

## Slide 15: Path Reference
v
Notes: The reference used is a helical trajectory, with the following equations of motion along the x, y, and z axes in terms of velocity and position. (Il riferimento utilizzato è un curva elicoidale con queste equazione del moto sugli assi x y e z in termini di velocità e posizione).

## Slide 16: RL implementation
Observations: UAV State Variables
Actions: Parameter
Notes: The RL takes the UAV states as input and outputs an action, which is a parameter η. Starting from an initial tuning value, these equations are used to dynamically update the controller gains. "Il RL ha come ingresso gli stati del UAV e come azione un parametro eta. Partendo dal un valore inziale di tuning, come queste equazioni vengono aggiornati in maniera dinamica i guadagni del PD“. In project we change in adaptive way only the gains of the outer loop. We fixed gains of the inner loop

## Slide 17: RL Reward Function
The reward function was defined as a weighted sum of the position, velocity, and attitude error norms:
The reward function is set as the following piece-wise function:
function R = calculate_R(error)
if error >= 11.5
R = -25;
elseif error >= 10.5 && error < 11.5
R = -15;
elseif error >= 9.5 && error < 10.5
R = -10;
elseif error >= 8.5 && error < 9.5
R = -5;
elseif error >= 7.5 && error < 8.5
R = -1;
elseif error >= 6.5 && error < 7.5
R = 10
else
R = 15;
end
end
Notes: The reward function was defined using a weighted sum of the position, velocity, and attitude errors and at the right side there is the code for the reward function. (La funzione reward è stata definita utilizzando una somma pesata dell'errore di posizione, di velocità e di assetto.)

## Slide 18: RL Block Scheme
Notes: This is the block diagram of the RL system. The way we update the gains and the reward function. The displays were used to monitor its operation, the reward function and the way the data is updated.
Questo è lo schema ha blocchi del RL. I display sono stati utilizzati per monitorare il funzionamento. Il modo in cui aggiorniamo i dati e la funzione reward

## Slide 19: RL Training Phase
Notes: "Questo è uno scope della posizione del drone con i suoi riferimenti. In matlab possiamo avviare la frase di training e monitorare il suo funzionamento"This is a scope of the drone’s position with its references. In MATLAB, we can start the training phase and monitor its performance."

## Slide 20: Results:Position tracking

## Slide 21: Results:Velocity tracking
Notes: These are the obtained results. The algorithm found the optimal gains to improve position and velocity tracking.
Questi sono i risultati ottenuti. L'algoritmo ha trovato i guadagni ottimi in modo migliorare il tracking di posizione e di velocità

## Slide 22: Results:Error Position tracking
Notes: The graphs show how the error converges to zero faster compared to manual tuning interms of position and velocity tracking.

## Slide 23: Results:Error Velocity tracking
Notes: I grafici mostrano come l'errore converge piu' velocemente a zero rispetto al tuning manuale

## Slide 24: Results:Position tracking with measurement error
Notes: To make the system more realistic, measurement noise was introduced in the two control loops. These are the results obtained; here as well, tracking improves and the error converges to zero more quickly using RL.
Per rendere il sistema piu' realistico è stato introdotto del rumore di misura nei due loop di controllo. E questi sono i risultati ottenuti, anche qui abbiamo un miglioramento del tracking e l'errore converge piu' velocemente a zero.

## Slide 25: Results:Error Position tracking with measurement error

## Slide 26: Results:The outer loop controller gains of RL-based controller
Notes: This plot shows how the gain values were obtained. In questo plot viene mostrato come sono stati ottenuti i valori dei guadagni

## Slide 27: Wind
Sum of Gaussians with varying mean and variance
Velocity Disturbance
Notes: To make the system more realistic, a disturbance, such as wind, was introduced in the form of a velocity disturbance. Sempre per rendere i sistema piu' realistico è stato introdotto un disturbo come il vento in termini di disturbo di velocità. The disturbance was added on x and y axis.

## Slide 28: Results: Position tracking with measurement errore & disturbance velocity
Notes: The following shows the results.

## Slide 29: Results: Error Position tracking with measurement errore & disturbance velocity
Notes: In the training phase was not concidered the meas error and the disturdance

## Slide 30: The outer loop controller gains of RL-based controller with disturbance of wind
Notes: The graph below shows the variations in the gain values under the influence of the disturbance. ( Nel grafico sotto viene mostrato come cambiano i valori dei guadagni con la presenza del disturbo. )

## Slide 31: DDPG vs TD3 vs SAC Training Phase
Notes: Finally, a comparison was made between the three algorithms, where SAC converges more quickly and is more stable, (due to the use of a piecewise reward function). Alla fine è stato fatta una confronto tra i 3 algoritmi dove il SAV converge piu' rapidamente ed è piu' stabile dovuto al fatto di avere utilizzato una funzione a tratti come reward. It was used the hyperparameters that are displayed in the table.

## Slide 32: 3D Animation
Notes: These are a 3d animation of UAV wirh 3 algorithms with a disturbance at time twenty

## Slide 33: Questions?